## Slide 1: Penn Center for Quantitative Echocardiography AAML 1831 Sonographer Office Hours January 24, 2023

## Slide 2: Welcome!
We have received over 1,000 echoes for this study to date. Quantitation is ongoing, with 750 echoes analyzed so far.
Thank you for your commitment and dedication to the clinical care of your patients and the advancement of cardio-oncology science!

## Slide 3: Objectives
To understand the importance of obtaining high quality echo images.
To discuss the differences in 2D and strain measurement techniques.
To improve proficiency in strain imaging acquisition.

## Slide 4: What views do we need? 2D and Strain
Apical 4-chamber
Apical 3-chamber (long axis)
Apical 2-chamber
RV focused

## Slide 5: Why do we need these views?- 2D
We are using the Simpson biplane method to measure LV volumes and calculate ejection fraction.
Please acquire high quality apical 4-chamber and apical 2-chamber views for this calculation.
(J Am Soc Echocardiogr 2010;23:465-95.)

## Slide 6: What is strain?
Strain measures LV deformation in longitudinal, radial, and circumferential directions.
Strain represents the percent change in LV fiber length from relaxed to contractile state.
https://doi.org/10.1016/j.jaccao.2020.10.011

## Slide 7: Why is strain important to us?
LVEF lacks sensitivity to detect subclinical changes in cardiac function caused my myocyte damage due to cardiotoxic treatment.
Global longitudinal strain (GLS) is a more sensitive and reproducible measure of LV systolic function, is an early marker of cardiotoxicity, and is the optimal deformation parameter for the detection of subclinical LV dysfunction.

## Slide 8: Common pitfalls in image acquisition
Liu J, Barac A, Thavendiranathan P, et al. Strain Imaging in Cardio-Oncology. J Am Coll Cardiol CardioOnc. 2020 Dec, 2 (5) 677–689.https://doi.org/10.1016/j.jaccao.2020.10.011

## Slide 9: Avoiding pitfalls in image acquisition
It is critical to include both the epicardium and endocardium throughout systole and diastole for strain analysis.
Please acquire high quality apical 4-chamber, 2-chamber, 3-chamber, and right ventricular views.

## Slide 10: Apical 4-chamber view
Please optimize your image to include a full view of all 4 chambers, including full visualization of the atria.
Then, adjust sector size and depth to include only the ventricles (please acquire images of the LV and RV separately).
The myocardium should be visible uniformly from the apex to the AV valves.

## Slide 11: Apical 4-chamber view

## Slide 12: Apical 2-chamber view
From the 4-chamber view, rotate the transducer approximately 60 degrees counterclockwise.
The left atrium, mitral valve, and left ventricle should be shown.
Adjust the sector size and depth to only show the left ventricle.

## Slide 13: Apical 2-chamber view

## Slide 14: Apical 3-chamber view
Also known as the apical long-axis view.
From the apical 2-chamber view, continue rotating the transducer approximately 60 degrees counterclockwise.
The left atrium, mitral valve, left ventricle, aortic valve, and aorta should be shown.
Adjust sector size and depth to only show the left ventricle.

## Slide 15: Apical 3-chamber view

## Slide 16: RV focused view
Starting in an apical 4-chamber view, rotate the transducer slightly counterclockwise.
Maximize the visualized area of the RV, avoiding tilting anteriorly into a 5-chamber view.
Tilting the transducer or sliding medial/lateral or into a different rib space may be necessary in some patients.

## Slide 17: RV focused view

## Slide 18: Example
Right Ventricle
At first glance, this image may look acceptable given that all segments are shown within the sector.
Sometimes, we are able to provide 2D measurements even when image quality is suboptimal for strain.

## Slide 19: Example: Right Ventricle- 2D

## Slide 20: Example: Right Ventricle- Strain
Although RV area was measured, the strain is not tracking
The RV free wall is too dark and the speckles are not being recognized
This strain will be reported as “not analyzable”

## Slide 21: Example: Right Ventricle
RV focused view showing all segments within the sector
Frozen end diastole
Frozen end systole
Endocardial borders are not well defined and RV area may be deemed “not analyzable.”

## Slide 22: Example: Apical 4-chamber
Endocardial borders are seen well enough to measure LV volume. Epicardial borders are not seen within the sector and stain may be reported as “not analyzable.”

## Slide 23: Example: Apical 2-chamber
Endocardial borders may be seen well enough to measure LV volume. Epicardial borders are not seen within the sector and stain may be reported as “not analyzable.”

## Slide 24: Analyzability Factors
Challenging patient population.
Strain is dependent on image quality.
Protocol- use your sonographer checklist.
Lack of ECG tracing.

## Slide 25: Image Optimization
Please optimize each image as best you can.
You may want to use tools such as:
  Harmonic Imaging- maximize signal-to-noise ratio
  Dynamic Range/Compression- appearance of shades of gray
  Sector Size and Depth- increasing frame rate
  Focus- improve resolution
  Overall Gain and TGC - equalize the appearance of structures across the entire sector

## Slide 26: Image Optimization
Maintain a high quality ECG throughout the study. Strain will always be marked as “not analyzable” without an ECG tracing.
Record at least 3 beats per clip. If the heart rate is ≥ 100bpm, then at least 5 beats per clip.
Utilize proper patient positioning and breathing maneuvers.
2D gain: It is preferable to overgain than undergain.
Record images at 50-70 frames per second.

## Slide 27: Image Optimization
Ensure that sector angle is not excessively narrow -narrowing results in cropping of LV apical segments and limits quantitation. Consider widening image sector width in order to include all wall anatomy.
Ensure endocardium and epicardium are visualized throughout entire cardiac cycle.
Avoid foreshortening: maximize cavity lengths in apical imaging planes.

## Slide 28: Please Use Your Sonographer Checklist!
Although this training was focused on 2D imaging, it is important to follow the protocol and acquire all required Doppler images as well.

## Slide 29: Feedback form
We have updated our feedback form to include space for comments.
We are providing more specific comments in the hopes of helping our sonographer community.
We always appreciate any feedback you have, and are always willing to help in any way we can.

## Slide 30: Thank you
Contact: aaml1831cardiacstudies@seattlechildrens.org